## Slide 1: IC Chip: Automated Clay Target Scoring System
Team Members:
Eva Kuntz - SE
Keith Snider - SE
Cole Huinker - CPrE
Steven Sleder - CPrE
Michael Ruden - EE
Philip Hand - EE
sdmay19-08
2 MAY 2019
Client & Advisor: Dr. Henry Duwe, ECpE
Notes: Eva

## Slide 2: Problem
No automated scoring method for clay shooting sports (i.e. Skeet Shooting).
Current scoring requires individual with:
  Exceptional eyesight
  Knowledge about sport procedures and rules
Finding willing human referees is difficult
Skeet Shooting Tournament.
Public Domain: https://free-images.com/display/shooter_shooting_gun_rifle.html
Notes: Steven

## Slide 3: Importance of IC Chip
Similar Product: ShotKam
  Camera attached to shotgun barrel.
  Accompanying mobile app.
  Tracks barrel movement.
  Slow-motion replay.
Why it won’t solve our problem:
  Expensive ($695/ShotKam)
  Have to reattach ‘kam’ to each shooter’s gun.
  Camera too narrowly focused.
  Does not classify targets!
Notes: Eva

## Slide 4: Operating Environment
Outdoor skeet shooting range
  Various weather conditions
  Strong wind v. light breeze
  Day v. Night
Hazards:
  Stray clay target pieces
  Shotgun pellets
  Range debris
Skeet Shooting Field.
Free Non-Commercial Use via Flicker User MichaelK91
Notes: Mike

## Slide 5: System Conceptual Sketch
System Conceptual Sketch.
Notes: Steven

## Slide 6: Functional Decomposition
System Function Decomposition
Notes: Cole

## Slide 7: Functional Requirements: Ground Station
The physical device should…
Produce its own WiFi signal.
Be accompanied by a protective, yet removable housing
Classify a clay target as DEAD or LOST.
Distinguish between a clay target fragment and shotgun wad or other debris.
Notes: Eva
***Only presenting core project requirements

## Slide 8: Functional Requirements: Mobile Application
The mobile application should...
Create and start shooting sessions.
Allow users to update scores in the scorecard.
Allow users to review video footage.
Allow users to challenge a target classification.
Allow users to start and stop the ground station from recording.
Allow users to exit and return to app w/o starting over
Notes: Eva

## Slide 9: Application Development
Xamarin.Android
Activities
Fragments
Models
Layout

## Slide 10: User Interaction
Android Application:
User creates and starts Shooting Session.
User controls shooting session
User can challenge target classification.
User views shot video only if target challenged.
User can overturn target classification.
Ground Station:
User sets up ground station.
User powers on ground station.
*Majority of user interaction is with mobile application!
Notes: Keith

## Slide 11: Adding Shooters to Session
Notes: Keith

## Slide 12: Shooting Session
Notes: Keith

## Slide 13: Video Review
Notes: Keith

## Slide 14: Backend
Flask
API calls to fetch data
Camera Control
Handled through the API
Analysis
Checks whether whether target came from high house or low house
Notes: Cole

## Slide 15: Backend Pipeline
Notes: Cole

## Slide 16: Model
AlexeyAB’s You Only Look Once, version 3
State-of-the-art object detection and tracking
Highly-tunable hyperparameters to fit limited resource requirements
Excellent solution for a supervised machine learning problem
Fork of the original algorithm with additional functionality and active maintainers
Excensible C/C++ Implementation
YOLOv3 in Action
YOLOv3 Resource Consumption
Notes: Steven

## Slide 17: Data Collection and Training
No Dataset Previously Existed
  Collected ~4 hours of raw video on two occasions
  Split into individual frames
  Manually label as Dead or Live
  8795 final labeled images
Split into Disjointed Training and Testing Sets
  6639 Training Images
  2166 Testing Images
  Approximately even distributions of Live and Dead
Training Times of 5-9 Days for Each Model
  Due to lack of compute resources
Nearly Satisfactory Performance on Testing Set
  91.4% for Live
  77.4% for Dead
Mean Average Precision and Prediction Accuracy
Notes: Steven - Training Data

## Slide 18: Hardware
Nvidia Jetson TX2 Developer Kit
  256 CUDA Pascal Cores
  8 GB LPDDR4
  Numerous ports for expansion
  Small footprint
e-CAM130 CUTX1
  Compatible w/ Jetson through high speed 4-lane MIPI CSI-2 interface.
  4912(H) x 3684(V) resolution
  72° FOV w/ changeable S-mount lens.
  Full capture control through software.
Jetson TX2 Developer Kit with mounted e-CAM130 CUTX1
Notes: Steven - Jetson
Mike - Camera

## Slide 19: Power Options
Power Adapter
  Wattage: 60W, Voltage: 19V, Amperes: 3.16 A
Battery Power Alternative
  2 x 5000 mAh LiPo 3s Batteries
  Capable of powering ground station 8 hours
Circuit Protections Needed
  Over Discharge Protection Circuit
  Overcurrent Protection circuit
Over Discharge Protection Circuit
Notes: Philip

## Slide 20: Looking Forward...
Algorithmically Handle Multiple Targets
  Ground station tracks what the current shooter’s position is
Examine and Improve the Robustness of the Model
  How well does it perform in real time on a live range?
  Is its performance invariant to different conditions such as lighting and background?
Additional System Integration
  Increase the functionality offered by the backend
  Fully integrate backend with the application.
Develop a Rugged System Housing
Battery added to Jetson
Notes: Steven, Keith, Cole

## Slide 21: Individual Member Contribution
Eva Kuntz
  Mobile Application design and development
  Project manager
Keith Snider
  Mobile Application development and testing
  Mobile Application requirements elicitation.
Cole Huinker
  Data collection lead
  Back end development
Steven Sleder
  Computer vision model construction
  Data labelling documentation and organization
Michael Ruden
  Camera selection
  Hardware Integration
Philip Hand
  Power
  Data labeling
Notes: ALL

## Slide 22: Questions?